## Slide 1: Could historical flood inundation be attributed to historical climate change or direct human influence?
Fang Zhao
12.14. 2021

## Slide 2: Introduction
As the observation techniques improve, more large floods are detected by satellite records in recent years. Tellman et al. (2021) also compiled a large global dataset of historical floods
It is unclear if the extent/magnitude of these historical floods is related to historical climate change or human management
ISIMIP3a simulation set-up allows for this examination

## Slide 3: Method
For our regional simulation focused river basins, first identify past flood events (either from previous literature, or Sentinel-1 SAR flood detection)
Use daily runoff maps from ~ 1990 (preferably earlier) to 2019, both from historical and counterfactual climate experiments, from the regional modeling teams (also simulate with CWatM for other basins for better global coverage)
Drive CaMa-Flood with these daily runoff to simulate historical flood inundations for large flood events, and detect if there is a trend in inundation extent for the river basins
Notes: Ganges, Indus, Godavari, Amazon, Darling

## Slide 4: Expected Results
Models driven by historical climate data may roughly capture observed flood extent
Models driven by counterfactual climate data may simulate smaller extent and magnitude of flood in some events
Question: could we determine if historical management (land use change, water withdrawal) affect simulated flood extent as well? Something like 1901soc, or perhaps natural experiment is fine too

## Slide 5: Challenges
Identify the flood events (focus basins mostly cover areas with not too much human influence)
Large requirement of simulated daily gridded runoff data (could all regional models interpolate to gridded runoff?)
Simulate these events reasonably well under histsoc/histclim (calibration should still make a difference, although CaMa-Flood will be used)