## Slide 1
Detection and attribution of hydrological changes in Arctic river basins: methodological aspects
Olga Nasonova, Yeugeniy Gusev, Evgeny Kovalev
Water Problems Institute, Russian Academy of Sciences, Moscow
Notes: 2

## Slide 2
Arctic river basins
RUSSIA

## Slide 3: Schematization of the river basins
The basins were presented as a set of regular grid cells (with a spatial resolution 0.5°0.5° in latitude and longitude) connected by a river network.
River basin | Streamflow gauge station |  |  | Area, km2 | Number of grid cells
 | Name | Latitude | Longitude |  | 
Northern Dvina | Ust’-Pinega | 64.13 | 42.17 | 348000 | 248
Taz | Sidorovsk | 66.60 | 82.28 | 100000 | 88
Indigirka | Vorontsovo | 69.58 | 147.35 | 305000 | 243
Northern Dvina
Taz
Indigirka

## Slide 4: Land surface model SWAP
Warm season
Cold season
Water balance components
Heat balance components

## Slide 5: Meteorological forcing data
♦ Incoming shortwave radiation
♦ Incoming longwave radiation
♦ Precipitation
♦ Air temperature
♦ Air humidity
♦ Wind speed
♦ Air pressure
ISIMIP3a: historical daily data for 1901-2019
 factual – «obsclim»
 counterfactural – «counterclim»

## Slide 6: Hydrological observations
River runoff at the basin outlets of the
 Northern Dvina (1957 – 2003)
 Taz (1962 – 1996)
 Indigirka (1950 –1994)
Snow water equivalent (SWE) – 1966-2019
Notes: 16

## Slide 7: Model parameters
Vegetation parameters (vegetation class, LAI, albedo, roughness length, greenness fraction, vegetation height, rooting depth) were taken or derived from the ECOCLIMAP database.
Soil parameters (porosity, field capacity, wilting point, hydraulic conductivity at saturation, soil matric potential at saturation and B-parameter in parameterisation by Clapp & Hornberger were calculated with equations by Cosby et al. and data on soil texture (CLAY and SAND) from ECOCLIMAP.
Calibrated parameters:
 Adjustment factors for
• soil hydraulic conductivity at saturation K0 ;
• rooting depth hr .
 Coefficient kh0 for soil column depth in h0 = kh0 hr .
 Adjustment factor for snow free albedo of the land surface albsum.
 Albedo of fresh snow albsn.
 Manning coefficient n.
 Effective velocity of water movement in a channel network ue.
Notes: 16

## Slide 8: Calibration and validation
Objective function:
Condition: Bias 5%
SCE-UA - Shuffled Complex Evolution method
Observations: 1) river runoff at basin outlets
2) SWE
Notes: 16

## Slide 9: Simulating river runoff and SWE
Analysis of the results
Paper
ISIMIP3a: historical daily data for 1901-2019
 factual – «obsclim»
 counterfactural – «counterclim»
Notes: 16

## Slide 10
Thank you!