## Slide 1: Update on climate change impacts in West Country
Fred F. Hattermann, Potsdam Institute for Climate Impact Research

## Slide 2
Outline
Climate change in West Country
Impacts on water, vegetation and extremes
Main messages

## Slide 3: Temperature Projections – West Country Region
Workshop II: West Country Region - Climate vulnerability, Impacts and Projections
Projected climate changes for the West Country Region relative to 1991-2020
Strong temperature increase over 21st century relative to current conditions.
Increase depends much on the emission scenario → Time for action!
Data: ISIMIP 3b
warm
cold

## Slide 4: Temperature Projections – West Country Region
Workshop II: West Country Region - Climate vulnerability, Impacts and Projections
Strong temperature increase over 21st century relative to current conditions.
Increase depends much on the emission scenario → Time for action!
Next 30 years: ~ 1.0 °C
Temperature increase stronger in summer (~ 1.5 °C in Aug) than in winter (~ 0.7 °C in Dec).
Projected climate changes for the West Country Region relative to 1991-2020
Data: ISIMIP 3b
warm
cold

## Slide 5: Precipitation Projections – West Country Region
Workshop II: West Country Region - Climate vulnerability, Impacts and Projections
Projected climate changes for the West Country Region relative to 1991-2020
Little variation in rainfall projections.
→ All is well?
Data: ISIMIP 3b
dry
wet

## Slide 6: Precipitation Projections – West Country Region
Workshop II: West Country Region - Climate vulnerability, Impacts and Projections
NO!
Summer becomes drier (drought risk?)
Winter becomes wetter (flood risk?)
Large uncertainties in projections (caused primarily by climate models rather than emission scenarios).
Projected climate changes for the West Country Region relative to 1991-2020
Little variation in rainfall projections.
→ All is well?
Data: ISIMIP 3b
dry
wet

## Slide 7: PROJECTIONS – WEST COUNTRY REGION (RECAP)
Workshop II: West Country Region - Climate vulnerability, Impacts and Projections
According to projections, the West Country Region is likely to deal with
>
Hotter summers
And milder winters
The increase of average temperatures will depend on emissions
Wetter Winters
Drier summers
No clear changes in overall precipitation averages
DROUGHT RISKS
HEATSTRESS RISKS
Heatstress, drought and flood will be more remarkable and recurrent in the region
FLOOD RISKS

## Slide 8
West Country
Impacts on water availability, vegetation and extremes

## Slide 9
Impacts on river discharge and extremes

## Slide 10: First step: Investigation of observed discharge (River Exe)
Daily discharge River Exe [m3/s]
Return period [a] Discharge [m3/s]
5 161.5
10 184.8
25 214.2
50 236.0
100 257.7
250 286.2
Observed discharge and extremes (River Exe)
Flood statistics

## Slide 11: River Exe, development of river discharge
Trend in annual discharge (River Exe)

## Slide 12: Eco-hydrological model SWIM
Weather / climate (input)
  Precipitation (rain & snow)
  Temperature, solar radiation, rel. humidity
Hydrology
  Infiltration
  Runoff: surface, sub-surface, groundwater
  River discharge
  Evapotranspiration
Vegetation
  Natural: forests, grasslands, savannah...
  Managed crops
Glaciers
Natural processes

## Slide 13: Eco-hydrological model
Water and land management
Crop management
  Crop rotations
  Fertilization
Irrigation
  Crop water demand / deficits
  Water use efficiency
Water allocation
Reservoirs
  Hydropower
  Flood protection
  Water supply

## Slide 14: Spatial data
European Soil Map
CORINE land use map
Digital Elevation Model of 100 m resolution
Climate data of European Weather Service
ISIMIP climate scenario data
Basic GIS layers
Hydrotopes (HRUs)
Elevation, slope (DEM)
Land use / cover (LULC)
Soils
Other
Natural, managed
Reservoirs, irrigation,
wetlands, glaciers, elevation
Climate input

## Slide 15: Rivers and observed stations considered in the model set-up
No of catchments: 344 No of subbasins: 1630
No of hydrotopes: 47948
No. of discharge station: 167

## Slide 16: Comparison of observed and modeled discharge
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
SWIM was applied for 344 river catchments in GB, including 4 located in Westcountry:
River Tamar
River Torridge
River Taw
River Exe
(Global multi-goal calibration using observed discharge at XYZ stations and sattelite ET data)
Example: River Exe – modelled and observed discharge [m3/s]

## Slide 17: Projected annual and seasonal discharge (River Exe)
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Development of annual discharge until end of the century (River Exe)

## Slide 18: Projected annual and seasonal discharge (River Exe)
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Development of monthly discharge (River Exe)
Development of monthly discharge (River Tamar)

## Slide 19: Development of flood hazard – hot scenario
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
River Exe – change in flood return levels high end scenario
Strong increase in flood risk mid – end of century
Projected changes in flood hazard (River Exe) – hot scenario RCP585
More
More
often

## Slide 20: Development of flood hazard – green scenario
Projected changes in flood hazard (River Exe) – green scenario RCP126
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
River Exe – change in flood return levels high end scenario
After increase until mid of the century a slow decrease in flood hazard
River Exe – change in flood return levels low-end scenario

## Slide 21: Development of flood hazard – hot scenario
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
River Tamar – change in flood return levels high-end scenario
Strong increase in flood risk mid – end of century
Projected changes in flood hazard (River Tamar) – hot scenario RCP585

## Slide 22: Development of flood hazard – green scenario
Projected changes in flood hazard (River Tamar) – green scenario RCP126
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
After increase until mid of the century a stronger decrease in flood hazard
River Tamar – change in flood return levels low-end scenario

## Slide 23: Change in hydrological processes at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Soil water flows and vegetation growth (arable land)
1971-2000
2071-2100
precipitation

## Slide 24: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Surface runoff
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 25: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Groundwater recharge
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 26: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Evapotranspiration
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 27: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Leaf Area Index
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 28: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Leaf Area Index
Soil water
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 29: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Leaf Area Index
Water stress
Soil water
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 30
Impacts on water quality

## Slide 31: Impacts on water quality
Change in nutrient flows (total nitrogen):
Past: High losses in winter with percolation
Losses
Plant uptake
Very management dependent
Second crop? Fertilizer regime?
Cover crops are relevant

## Slide 32
Impacts on health and outdoor productivity

## Slide 33: Simulations and projections
Health: Wet Bulb Globe Temperature
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Wet Bulb Globe Temperature (WBGT) is a measurement used to assess the risk of heat related illnessess due to exposure to the current temperature, humidity, wind speed and solar radiation parameters.
Max WBGT corresponds to the daily maximum values of WBGT.
< 25.6°C - 27.7°C = White: 5 min rest every 30 min
27.8°C - 29.4°C = Green: 5 min rest every 25 min
29.5°C - 31°C = Yellow: 5 min rest every 20 min
31.1°C - 32.1°C = Red: 5 min rest every 15 min
> 32.2°C = Black: Suspend athletic activities recommended

## Slide 34: SWIM model simulations and projections
Outdoor productivity
Workshop II: Egaleo – Climate vulnerability, Impacts and Projections
Labor productivity denotes the maximum potential work output achievable by an individual in a day. This measure is represented as a percentage (%) to indicate the proportion of work that can be achieved under current climatic conditions. It is mainly derived from the impact of heat on productivity, as exposure to heat stress tends to diminish the average worker's capacity to perform tasks efficiently.
There are 4 different levels of labor productivity levels, each corresponding to a certain amount of work intensity:
200W = Low intensity work
300W = Medium intensity work
400W = High intensity work
500W = Very high intensity work

## Slide 35
Summary
Hotter summers and warmer winters -> extension of the vegetation period and increasing water vegetation demand (EvapoTranspiration)
Wetter winters and drier summers -> drier soils in summer, more water stress, but in winter increase in groundwater recharge leading to more water in rivers (also in summer)
More intense precipitation -> increase in flood number and intensity, more surface runoff, more erosion and phoshorous losses. Riparian zones and wetlands to counteract
Longer vegetation period -> two crops? But wetter soil conditions in spring and fall may lead to problems with cultivation. Increasing Temperature/vegetation period may foster biotic risks (Pest and diseases)
More vegetation in winter -> May lead to more nutrient (nitrate) uptake and reduce losses with percolation. Cover crops in winter are important.
Higher water temperatures in rivers -> stimulate algae growth and blooming
Cropping and fertilization schemes have to be adapted accordingly

## Slide 36
Thanks!
Any questions?