## Slide 1: Fred F. Hattermann Potsdam Institute for Climate Impact Research hattermann@pik-potsdam.de
Earth System Analysis & Stewardship

## Slide 2: Key questions addressed
Why is water so relevant?
What is the role of water in the climate cycle?
Which processes are important?
What are the interactions with vegetation?
How can the water cycle and the water nexus be modelled?
What are possible adaptation measures and strategies?

## Slide 3: What we will do
Theory Background and conceptualization
Examples Modelling and interpretation
Application Presentation of selected topics

## Slide 4: The water nexus, processes and interpretation
Soils
Climate
Water
Energy
Vegetation

## Slide 5: Solutions

## Slide 6: Outline
Monday Nov. 18
The water cycle: From hydrological processes to observations,
presentation of topics, groupwork
Tuesday Nov. 19
The nexus water – energy – food. Water as a basic need, water as a threat: health, hydrological extremes, erosion,
Selection of topics, groupwork
Wednesday Nov. 20
Eco-hydrological modelling,
Groupwork
Thursday Nov. 21
Groupwork
Friday Nov. 22
Presentation of selected tasks, visiting PIK

## Slide 7: Water is life
Nearly 97% of the world’s water is salty or otherwise undrinkable. Another 2% is locked in ice caps and glaciers. That leaves just 1% for all of humanity’s needs.
Water regulates the Earth’s temperature and the temperature of the human body, carries nutrients and oxygen to cells, and removes wastes.
75% of the human brain is water and 75% of a living tree is water.
A person can live about a month without food, but only a few days without water.

## Slide 8: Water can be a threat
Water is a problem, when
having too much;
having too low;
having water of low quality.

## Slide 9: Properties of water
Dipol
Wassermolekül, Wikimedia Commons contributors, CC BY-SA.
Wasserläufer auf Wasseroberfläche, Wikimedia Commons contributors, CC BY-SA.
Water surface tension
Kapillary effect
Kapillareffekt beim Wasser, Wikimedia Commons contributors, verändert, CC BY-SA.
Wasserstoffbrückenbindung, Wikimedia Commons contributors, public domain.
Aus: Fohrer, 2016.

## Slide 10: Conversion millimeter into litre
4. Niederschlag I
4.2 Niederschlagsmessung
1 mm (rain) = 1 litre / m2

## Slide 11: Repetition: Energy distribution on Earth’s surface
Earth
High latitudes receive light at low angles
Regions near the equator receive light at 90o
-> Light energy is more concentrated near the equator. In other words, there is a greater flux per unit area (W/m2)

## Slide 12: Excess energy at the equator is transferred towards the poles by convection cells
Energy
90 45 0 45 90
Latitude
net radiation
surplus
net radiation
deficit

## Slide 13
The rising air creates a circulation cell, called a Hadley Cell
solar radiation
L
H
Rising air -> low pressure
Sinking air -> high pressure
H

## Slide 14: Global Atmospheric Flux and Ciculation Cells
Credit: NASA

## Slide 15: Energy Transport in the Earth System
Solar energy received is greatest near the equator.
Energy is moved from the equator to the poles.
Energy is transferred by wind and ocean currents and these are coupled!
Examples: Monsoon and ENSO

## Slide 16: Water cycle, simple
Main processes:
Precipitation
Evaporation
Condensation
Driver:
Solar radiation
Gravity

## Slide 17
Is this climate change?

## Slide 18: Global water trends
Pascolini-Campbell et al (2021)
Evapotranspiration
Precipitation
Runoff
Groundwater
Gravity Recovery and Climate Experiment (GRACE)
Notes: Pascolini-Campbell, M. et al. (2021) A 10 per cent increase in global land evapotranspiration from 2003 to 2019, Nature, doi:10.1038/s41586-021-03503-5

## Slide 19: Number of events worldwide (Munich Re NatCat)
Number!

## Slide 20: Hydrological tasks
After Dyck & Peschke (1995):
Exploration of the water cycle
Calculation of the water balance over different scales (earth, continents, river basins, water management systems) for different periods of time
Determination of water resources (usable share of groundwater and surface water)
Hydrological forecasts (water level, runoff, groundwater recharge, ice)
Investigation of runoff regimes (especially extreme runoff)
Use and management of water ressources

## Slide 21: Literatur
Maidment, D.R. (1993): Handbook of Hydrology, McGraw-Hill, New York.
Fohrer, N. (2016): Hydrologie. Utb Taschenbuchreihe. (Sehr gutes Lehrbuch für „Einsteiger*innen“).
Dyck, S. & Peschke, G. (1995): Grundlagen der Hydrologie, 3. Auflage, Verlag für Bauwesen, Berlin.
Baumgartner, A. & Liebscher, H.J. (1996): Allgemeine Hydrologie: quantitative Hydrologie, 2. Auflage, Borntraeger, Stuttgart.
Nützmann, G. & Moser, H. (2016): Elemente einer analytischen Hydrologie. Springer Verlag. (sehr aktuell, gute Abbildungen, verständlich)
Wohlrab, B., Ernstberger, H., Meuser, A., Sokollek, V. (1992): Landschaftswasserhaushalt. Verlag Paul Parey Berlin. 352 S. Fachübergreifendes Lehrbuch, das Bezug auf die Wasserhaushaltskomponenten auf der Landschaftsebene Bezug nimmt. Umfassende Begriffsdefinitionen.
Maniak, U. (2005): Hydrologie und Wasserwirtschaft: Eine Einführung für Ingenieure. 5. Aufl., Springer, Berlin. Grundlagen zum Wasserhaushalt, sehr viel hydrologische Modellierung.

## Slide 22: „The hydrological classics“
The water cycle
Precipitation
Evapotranspiration
Discharge
Storage

## Slide 23
1. The water cycle

## Slide 24: Definition (DIN 4049)
Water cycle
Continuous sequence of changes in the state and location of water with the main components precipitation, runoff, evaporation and atmospheric water vapour transport.
Water balance
Quantitative recording of the components of the water cycle and the change in supply in an area under consideration during a period of observation.

## Slide 25: Water balance, global
Globale Wasserbilanz aus Fohrer (2016), Zahlen nach Korzun (1978).
Roughly:
Ca. 3 % freshwater, of that:
  2/3 in glaciers
  1/3 in groundwater
  < 1 % surface water (directly usable)

## Slide 26: Water cycle, simple
Main processes:
Precipitation
Evaporation
Condensation
Driver:
Solar radiation and gravity

## Slide 27: Water balance equation
Evaporation
Precipitation
Discharge
=
+
+
+/- storage

## Slide 28: Water cycle, global
The global water cycle. Illustration: GIZ (2020) with data from Trenberth et al. (2011).
Water reservoirs
Oceans, inland waters, glaciers, groundwater, atmosphere, soil water, organisms ...
Processes
Precipitation,
evaporation,
seepage,
Runoff

## Slide 29: Water balance Brandenburg
Precipitation ~600 mm
Evapotranspiration ~500 mm
Runoff/ Discharge ~100 mm
+/-Storage

## Slide 30: Precipitation in Germany
Data: Wodinski, Gerstengarbe and Werner, PIK Potsdam
Mean precipitation 1951-2003
Trend in precipitation 1951-2003

## Slide 31: Components of the water balance Germany
Evapotranspiration
Runoff
GW-recharge
Huang et al. 2010

## Slide 32: Seasonal water balance Elbe EZG
Evapotranspiration
Precipitation
Discharge
Elbe

## Slide 33
2 Precipitation

## Slide 34: Precipitation
2.1 Formation of precipitation
2.2 Precipitation monitoring
2.3 Precipitation in Germany and global

## Slide 35
2 Precipitation
2.1 Formation of precipitation

## Slide 36: Water cycle, simple
Main processes:
Precipitation
Evaporation
Condensation
Driver:
Solar radiation and gravity

## Slide 37: Conversion millimeter into litre
4. Niederschlag I
4.2 Niederschlagsmessung
1 mm (rain) = 1 litre / m2

## Slide 38: Water cycle, global
The global water cycle. Illustration: GIZ (2020) with data from Trenberth et al. (2011).
Water reservoir
Oceans, inland waters, glaciers, groundwater, atmosphere, soil water, organisms ...
Processes
Precipitation,
evaporation,
seepage,
Runoff

## Slide 39: Definition of precipitation
Precipitation is generally understood to be the water precipitated from the atmosphere that has previously passed from the gaseous phase (water vapour) into the liquid or solid phase.
In meteorology, a distinction is made between precipitation that has settled on surfaces (dew, hoarfrost, etc.) and precipitation that is falling (rain, snow, hail, etc.).
Metéoron (Greek) means sky or air phenomena.
4. Niederschlag I
4.1 Entstehung von Niederschlag

## Slide 40: Definition of precipitation
40
According to DIN 1996, precipitation is: "Water of the atmosphere that has been formed in the air after condensation or sublimation of water vapour and, as a result of gravity, either moves to the earth's surface (falling precipitation) or has reached the earth's surface (settled precipitation)".
4. Niederschlag I
4.1 Entstehung von Niederschlag

## Slide 41: Formation of precipitation
4. Niederschlag I
4.1 Entstehung von Niederschlag
The three preconditions for the formation of precipitation:
Saturation of the air with water vapour (relative humidity > 100%). For this to happen, the temperature of the air must be equal to the dew point temperature*. This is usually the result of cooling experienced by a rising or expanding air parcel.
Phase transition (condensation, freezing).
Growth of droplets and ice particles (aerosols important).
* Dew point = temperature corresponding to the saturation vapour pressure. If temperature below dew point -> condensation, precipitation

## Slide 42: Calculation of saturation vapour pressure
For the calculation of the saturation vapour pressure Ew or especially for the phase transition liquid to gaseous, one can use the Clausius-Clapeyron equation. But it is difficult to integrate. Therefore, approximate solutions are applied, the simplest of which are the Magnus formulae:
For (flat) water surfaces:)
for
For (flat) ice surfaces: )
for
4. Niederschlag I
4.1 Entstehung von Niederschlag

## Slide 43: Some results of the Magnus formula
Temperature [°C] | -20 | -10 | 0 | +10 | +20 | +30
Saturation water content [g/m3] | 1,1 | 2,4 | 4,8 | 9,4 | 17,2 | 30,3
Saturation vapour pressure pv,s [Pa], 1 Pa = 1 N/m² | 124 | 285 | 611 | 1228 | 2339 | 4244
4. Niederschlag I
4.1 Entstehung von Niederschlag

## Slide 44: Saturated water content of the atmosphere is a non-linear function of temperature
q [g/m³]
q (18°C) - q (15°C) = 2.5 g/m³ (= 19,4 %)
4. Niederschlag I
4.1 Entstehung von Niederschlag

## Slide 45: Increase of intense precipitation with temperature
15min
?
Increasing extreme rainfall intensities through climate change
Bürger, Uni Potsdam, personal communication
15min precipitation,
99.9% Quantile,
Stations Brixenbachtal, Längental, Ruggbachtal

## Slide 46: Daily Rainfall Records Increase Globally
Lehmann et al., Climatic Change, 2015
88%
26%
The saturation vapour pressure regulates the daily amounts of heavy rainfall.
This increases at a rate of 7% per degree of warming (Clausius-Clapeyron).

## Slide 47
Precipitation types
Direct condensation or sublimation of water vapour at or near the earth's surface:
Liquid form: Dew (condensation)
Solid forms: Frost (resublimation), frozen dew
Falling precipitation: condensation or sublimation in the free atmosphere, precipitation from clouds:
Liquid form: Rain
Solid forms: Snow, hail, sleet
4. Niederschlag I
4.1 Entstehung von Niederschlag

## Slide 48: Frost
Source: Karlsruher Wolkenatlas

## Slide 49: Snow
Source: Karlsruher Wolkenatlas

## Slide 50: Hail
Source: Karlsruher Wolkenatlas

## Slide 51: Hail
Quelle: http://www.chaseday.com/hail.htm

## Slide 52: Advective (front) precipitation
4. Niederschlag I
4.1 Entstehung von Niederschlag
Typical precipitation types associated with a warm front advancing over cold air masses
https://www.stratusdeck.co.uk/fronts

## Slide 53: Advective (front)
Source: Karlsruher Wolkenatlas

## Slide 54: Convective

## Slide 55: Convective rain – thunder storms
Source: Karlsruher Wolkenatlas

## Slide 56: Orographic
https://www.slideshare.net/slideshow/types-of-rainfall/27227404#8

## Slide 57: Orographic
Source: Karlsruher Wolkenatlas

## Slide 58: Settled precipitation
This form of precipitation has its special significance in:
Cloud forests (e.g. Andes, Canary Islands)
Coastal deserts (e.g. Southwest Africa, Northern Chile)
4. Niederschlag I
4.1 Entstehung von Niederschlag

## Slide 59
2 Precipitation
2.2 Monitoring of precipitation

## Slide 60: Conversion millimeter into litre
4. Niederschlag I
4.2 Niederschlagsmessung
1 mm (rain) = 1 litre / m2

## Slide 61: Hellmann rain gauge (ombrometer)
200 cm2
4. Niederschlag I
4.2 Niederschlagsmessung
Reference area: 200 cm2
1 m above surface (snow free)
1,5 m above surface (snow)
https://www.spektrum.de/lexikon/geographie/hellmann-regenmesser/3425

## Slide 62: Undercatch
62
4. Niederschlag I
4.2 Niederschlagsmessung
Classical observartions techniques underestimate precipitation by 10-20% at least, due to:
the influence of evaporation and spray water,
snow bonnets, wind influence as well as wetting influence.
In addition, inhomogeneities in the environment interfere, e.g. with plant growth, high-rise construction.
Undercatch larger for snow
Empirical and physically based methods to correct exist

## Slide 63: Advanced rain gauges
Precipitation gauge based on the weighing principle with wind protection
Many types and variations exist
Often digital
Comparability!?

## Slide 64: Synoptic station
4. Niederschlag I
4.2 Niederschlagsmessung

## Slide 65: Observation network in Germany
4. Niederschlag I
4.2 Niederschlagsmessung
2242 stations before 2010
1218 stations since 2010

## Slide 66: Radar monitoring of precipitation
4. Niederschlag I
4.2 Niederschlagsmessung
Radar station of the DWD (Reach per station 150 km)
https://www.dwd.de/DE/leistungen/radarprodukte/radarprodukte.html

## Slide 67: Radar monitoring
Radar cannot directly measure the precipitation height.
The radar impulses reflected by raindrops only provide an areal distribution of the strength of the radar echoes. Since the strength of the backscatter depends on the size and quantity of the raindrops, the precipitation height can be calculated using empirical relationships and correction methods.
The radar data are calibrated by means of precipitation measurements on the ground.
The DWD radar network comprises 16 radar sites, each with a radius of 128 km, which ensure extensive coverage of Germany.
4. Niederschlag I
4.2 Niederschlagsmessung
https://www.dwd.de/DE/leistungen/radarprodukte/radarprodukte.html

## Slide 68: Radar monitoring
4. Niederschlag I
4.2 Niederschlagsmessung
[mm]
https://www.dwd.de/DE/leistungen/radarprodukte/radarprodukte.html

## Slide 69: Interpolation of point measurements
4.3 Niederschlagsauswertung Gebietsniederschläge
?

## Slide 70: Weighted mean and polygon method
4.3 Niederschlagsauswertung Gebietsniederschläge – Thiessen-Polygone (nächster Nachbar)

## Slide 71: Inverse distance
raster point
4.3 Niederschlagsauswertung Gebietsniederschläge – Inverse Distanz

## Slide 72: Inverse distance
Good for non-uniformly distributed stations, as an interpolation method for soft transitions
4.3 Niederschlagsauswertung Gebietsniederschläge – Inverse Distanz

## Slide 73: Inverse distance
Example (with p=1, n=2):
z(u1)=2
z(u1)=2
Z*(u0)=?
z(u2)=4
z(u2)=4
Z*(u0)=?
d1=5
d2=3
d1=8
d2=3
4.3 Niederschlagsauswertung Gebietsniederschläge – Inverse Distanz

## Slide 74: Isohyetes (zones of the same hight)

## Slide 75: Geostatistical methods
2) Data analysis
3) Variogram
4) Interpolation
with Kriging
5) Error analysis!
4.3 Niederschlagsauswertung Gebietsniederschläge – Geostatistische Verfahren
2) Observations

## Slide 76: Comparison of the methods

## Slide 77: Reanalysis data is another possible combination of spatial and point data
Weather forecast data and station data are combined;
In the process, a weighted combination of measured values and older model predictions is interpolated onto the model grid using various mathematical methods (so-called data assimilation);
In a numerical forecast model, the computational domain is discretised with grid cells so that the relevant physical quantities, such as temperature, precipitation, air pressure, density and wind speed, can be represented in three-dimensional space and as a function of time.

## Slide 78: Reanalysis data
Weather forecasts are available worldwide in high temporal and spatial resolution
They are constantly updated with observations (data assimilation)
(Source: European Meteorological Service)

## Slide 79: Example: Re-analysis data for Tanzania

## Slide 80: The COSTRA system of the DWD: Information about intense precipitation
https://www.dwd.de/DE/leistungen/kostra_dwd_rasterwerte/kostra_dwd_rasterwerte.html

## Slide 81
2 Precipitation
2.3 Precipitation in Germany and global

## Slide 82: Recent precipitation Potsdam
T
P
https://www.pik-potsdam.de/de/produkte/klima-wetter-potsdam/wetteranalyse

## Slide 83: Soil moisture station Potsdam

## Slide 84: Annual precipitation total (left) and trend (right)

## Slide 85: Seasonal distribution of precipitation
4.4 Niederschläge in Deutschland und Weltweit Niederschläge in Deutschland
Evapotranspiration
Niederschag
Abfuss
Elbe

## Slide 86: Global precipitation
Wasserkreislauf
2.2 Der globale Wasserkreislauf

## Slide 87: Precipitation records (annual)
Precipitation records |  |  |  | 
Continent | Land | Location | Value | Year
Europe | Croatia | Crkvice | 4648 mm | 1881
 | Germany | Balderschwang (Allgäu) Potsdam | 3503,1 mm 788,8 mm | 1970 1981
Africa | Kamerun | Debundscha | 10287 mm | 1932
America | USA | Paradise (Mt. Rainier) | 31100 mm (Snow) | 1970/71
 | Kolumbia | Lloro | 13299 mm | 1929
Asia | India | Cherrapunji | 26461 mm | 1860/61
Australia | Queensland | Bellenden Ker | 8636 mm | 1909
4.4 Niederschläge in Deutschland und Weltweit Extreme des Niederschlages

## Slide 88: Precipitation records (subannual)
Daily precipitation records |  |  |  | 
Continent | Land | Location | Value | When
Africa | La Reunion | Cilaos | 1870 mm | 15.03.-16.03.1952
Europe | Deutschland | Zinnwald Potsdam | 312.0 mm 105.7 mm | 12.08.2002 08.08.1978
Monthly precipitation records |  |  |  | 
Asia | Indien | Cherrapunji | 9300 mm | 1970/71
Europe | Deutschland | Oberreute (Bodensee) Potsdam | 777 mm 202.3 mm | Juli 1954 Juli 1907
Snow records |  |  |  | 
America | USA | Paradise (Mt. Rainier) | 31100 mm | 1970/71
Europe | Deutschland | Zugspitze Potsdam | 8300 mm 700 mm | 02.04.1944 1969/70
4.4 Niederschläge in Deutschland und Weltweit Extreme des Niederschlages

## Slide 89: Orographic precipitation La Reunion
La Reunion
Climate diagram Saint Denis/Reunion

## Slide 90: Group work: please answer the questions!
How is the global share of saltwater and freshwater?
What are the three main components of the water balance?
How much water is 600 mm of precipitation?
How is the water balance of Brandenburg?
What is undercatch of observed precipitation?
Is the saturated water content of the air a linear or non-linear function of T?
What is orographic precipitation?

## Slide 91
3. Evapotranspiration

## Slide 92: Evapotranspiration
4.1 Definition and processes
4.2 Monitoring
4.3 Evaporation in Germany and global

## Slide 93
3. Evapotranspiration
3.1. Definition and processes

## Slide 94: Definition
DIN 4049-3
Evaporation is a process in which water changes from the solid or liquid aggregate state to the gaseous state at temperatures below the boiling point.
Unit of measurement: mm/unit of time

## Slide 95: Evaporation
Boundary layer
When the molecules of a liquid collide, they transfer energy based on how they collide with each other.
When a molecule near the surface absorbs enough energy to overcome the vapour pressure, it will escape and enter the surrounding air as a gas.

## Slide 96: Water cycle, global
Der globale Wasserkreislauf. Darstellung: GIZ (2020) mit Daten aus Trenberth et al. (2011).

## Slide 97: Water balance Brandenburg
Precipitation ~600 mm
Evapotranspiration ~500 mm
Runoff/ Discharge ~100 mm
+/-Storage
Evapotranspiration:
Transpiration: ~50–70 %
Interception: ~15–40 %
Evaporation: ~5–25 %

## Slide 98: Water balance and energy balance are coulpled via evaporation
Energy balance | 
Rn + H + G + LE = 0 | 
Rn | Net radiation
H | Sensible heat flux
G | Ground heat flux
LE | Latent heat flux
Water balance | 
N + V + Q + ΔS = 0 | 
N | Precipitation
V | Evaporation
Q | Runoff
ΔS | Storage

## Slide 99: Evaporation - phase transformation
The following transition heats L*, which depend on the temperature, apply to phase transitions of the water.
At 0 °C they are:
solid fluent: L* = 333,6 kJ/kg
fluent gas: L* = 2 500,6 kJ/kg
solid gas: L* = 2 834,2 kJ/kg
As a comparison:
The heating of water from 0 °C to 100 °C (no change in the state of aggregation): 418 kJ/ kg.
~1/6 of the energy needed at the same initial temperature to complete the phase transition by evaporation

## Slide 100: Evapotranspiration
Foto: Prof. Miegel (Uni Rostock)
Evapotranspiration = Evaporation + Transpiration

## Slide 101: Evaporation
Evaporation happens from surfaces such as
Water surface
Soil without vegetation cover
Interception (from vegetation surface)
Snow surfaces

## Slide 102: Evaporation
Evaporation happens from surfaces such as
Water surface
Soil without vegetation cover
Interception (from vegetation surface)
Snow surfaces

## Slide 103: Evaporation
Water surface
Soil without vegetation cover
Interception (from vegetation surface)
Snow surfaces
Evaporation happens from surfaces such as

## Slide 104: Evaporation
Water surface
Soil without vegetation cover
Interception (from vegetation surface)
Snow surfaces
Evaporation happens from surfaces such as

## Slide 105: Transpiration
Transpiration is the evaporation from plant surfaces due to biotic processes.
It mainly involves the release of water through the stomata.
Plants are able to regulate this release by closing and opening the stomata.

## Slide 106: Plant evapotranspiration
Stomatal transpiration / stomatal resistance
In plants, water is generally released through special adjustable door cells called stomata. CO2 is absorbed through the same openings.
The extent of water release in different plant species can vary by more than two orders of magnitude.
The control of the stomata is regulated by the turgor (pressure of the cell).
In warm regions there are special adaptations for the transpiration of plants, because there the plant is always faced with the problem that it has to absorb CO2 through the stomata on the one hand, but also loses water again as a result.
To reduce this problem, many plants have, for example, sunken stomata with special hairs.

## Slide 107: Competition CO2 in H2O out
https://www.tasmeemme.com/
Net product respiration:
C6H12O6 + 6 O2 → 6 CO2 + 6 H2O
Net product photosynthesis:
6 CO2 + 6 H2O → C6H12O6 + 6 O2

## Slide 108: C3 and C4 plants
5. Verdunstung 5.2 Physikalische Grundlagen
C4 plants actively bind CO2 using additional energy.
This allows them to close the stomata further and consume less water per biomass produced.
However, they have a higher temperature optimum and are less energy efficient.

## Slide 109: Share [%] of the two components
Proportion of evaporation components on average in Central European landscapes:
Transpiration: ~50-70 %
Interception evaporation: ~15-40 %
Evaporation: ~5-25 %

## Slide 110: Effects on evaporation
Evaporation is physically dependent on the following factors:
Solar radiation as a source of energy
Air temperature (which in turn depends on solar radiation)
Air humidity and thus the saturation deficit of the air
Wind movement, especially its turbulence and thus the greater mixing of the air

## Slide 111: Potential and actual evapotranspiration
Potential evaporation (PE) or potential evapotranspiration (PET) is defined as the amount of evaporation that would occur if sufficient water is available.
Actual evapotranspiration (AET) is the net result of atmospheric demand for moisture from a surface and the ability of the surface to supply moisture.
Therefore, PET is a measure of the demand side, AET is limited by the supply.
A dryland is a place where annual potential evaporation exceeds annual precipitation.

## Slide 112: Potential evapotranspiration
Maximum possible evaporation of a site under given meteorological conditions with optimal water supply -> Conversion of the total energy supply
PET exclusively dependents on meteorological (atmospheric) variables (temperature, humidity, wind, radiation)
Examples of potentially evaporating surfaces:
Evaporation from free water surfaces (lakes, rivers ...)
Evaporation from moist soil (after rain events or during irrigation)
Evaporation from snow cover
AET = PET
(e.g. over lakes)

## Slide 113: Actual evapotranspiration AET
Value of evaporation actually occurring at a site
Depending on atmospheric, soil and vegetation conditions and availability of water
AET << PET
Even AET = 0
(during drought)

## Slide 114: Equations to calculate PET
The Penman equation describes evaporation (E) from an open water surface, and was developed by Howard Penman in 1948. Penman's equation requires daily mean temperature, wind speed, air pressure, and solar radiation to predict E.
The Penman–Monteith equation refines weather based potential evapotranspiration (PET) estimates of vegetated land areas. It is widely regarded as one of the most accurate models, in terms of estimates.
The Priestley–Taylor equation was developed as a substitute to the Penman–Monteith equation to remove dependence on observations.

## Slide 115
3. Evapotranspiration
3.2 Monitoring

## Slide 116: Evaporimeter
Evaporation kettles filled with water are used to determine the evaporation by measuring the decrease of the water level.
https://en.wikipedia.org/wiki/Pan_evaporation

## Slide 117: Lysimeter
Weighing Lysimeter
Principle: Measures changes in the weight of the lysimeter to determine water balance
Operation: The lysimeter is placed on a scale and changes in weight are recorded over time, allowing for the calculation of evaporation, transpiration, and drainage

## Slide 118: Lysimeter
Quelle: Fohrer, 2006
Lysimeter system in Groß Lysewitz
Lysimeter in Brandis (Sachsen)

## Slide 119: Lysimeter
Quelle: in Anlehnung an Schröder et al. 1994
https://en.wikipedia.org/wiki/Lysimeter

## Slide 120
3 Evapotranspiration
3.3 In Germany and global

## Slide 121: AET 1961-90 for Germany, hyd. atlas and modelled
121
Hydrological atlas Modelled (Model SWIM, PIK)
5. Verdunstung 5.5 Anteil der Verdunstung an der Wasserbilanz

## Slide 122: AET in Berlin
evaporation
http://www.stadtentwicklung.berlin.de/umwelt/umweltatlas/
5. Verdunstung 5.5 Anteil der Verdunstung an der Wasserbilanz

## Slide 123: Effects of vegetation cover
Chart: hV/hN in %
| Kategorie 1
Nackter Boden | 30
Getreideland | 40
Hackfrüchte | 45
Grünland | 65
Wälder | 70
freie Wasserfläche | 75
feuchte Erdoberfläche | 95
Ratio of annual evaporation to annual precipitation as a function of vegetation (exemplary)
Quelle: Nacken (RWTH Aachen)
Bare soil
Arable land (cerials)
Arable land (root crops)
Pasture
Forest
Water surface

## Slide 124: Influence of vegetation cover on water balance
Influence of vegetation cover (stand age in brackets) on the water balance of a pine and a beech forest near Eberswalde (annual precipitation 620 mm) compared to Grass.
Interception
Evapotranspiration
Groundwater recharge
Source: following Müller 2009
Beech (broadleef)
Pine (coniferous)

## Slide 125: Seasonal distribution of evapotranspiration
4.4 Niederschläge in Deutschland und Weltweit Niederschläge in Deutschland
Evapotranspiration
Precipitaion
Discharge
Elbe

## Slide 126: Potential evapotranspiration

## Slide 127: Actual transpiration

## Slide 128: Global water trends
Pascolini-Campbell et al (2021)
Evapotranspiration
Precipitation
Runoff
Groundwater
Gravity Recovery and Climate Experiment (GRACE)
Notes: Pascolini-Campbell, M. et al. (2021) A 10 per cent increase in global land evapotranspiration from 2003 to 2019, Nature, doi:10.1038/s41586-021-03503-5

## Slide 129
4 Discharge

## Slide 130: Discharge
4.1 Definition and processes
4.2 Monitoring
4.3 Discharge in Germany and global

## Slide 131
4 Discharge
4.1 Definition and processes

## Slide 132: Definition discharge and runoff
In hydrogeology, runoff (according to DIN 4049-1) is defined as water moving on and under the land surface under the influence of gravity.
In hydrology, discharge (abbreviation Q) is the volume of water leaving a catchment area under the effect of gravity within a certain time.
If the runoff is divided (normalised) by the EZG area, it is referred to as runoff donation.

## Slide 133: River types
http://homepage.hispeed.ch/heiner.brogli/Exo/omu/Geopage.htm

## Slide 134: Flow generation: boundary conditions
Area features
Relief
Soil properties
Geology
Groundwater conditions
Vegetation
Hydrometeorological conditions
Pre-humidity
Precipitation amount and intensity
Temperature
Evaporation
Proportion of snowfall
Presence of glaciers
Anthropogenic influences
Land use
Degree of sealing
Drainage system / sewerage

## Slide 135: Surface flow
Mechanisms:
Due to infiltration excess Rainfall intensity > Infiltrability of the soil Also known as Hortonian runoff (after Horton, 1933).
Through saturation surplus The ground surface is saturated and can no longer absorb water.
Return Flow Runoff that has briefly infiltrated and then exfiltrated back to the surface.
Quelle: Fohrer (2016).

## Slide 136: Interflow
= Water that flows to the water body through near-surface, (often) unsaturated soil layers.
Important processes:
Infiltration
Surface runoff, possibly with return flow
Rapid lateral runoff through preferential flow paths (macropores, root zone, gravel layer, etc.)
Matrix flow (soil matrix)
Quelle: Fohrer (2016).

## Slide 137: Groundwater discharge
= Water that reaches the saturated zone through percolation and flows to the watercourse following the gradient.
Slow process, provides most of the base flow.
Macropores (e.g. karst) can also lead to rapid groundwater recharge and thus also to the contribution of groundwater during runoff events
QBHW: Basisabfluss bei Hochwasser. QBTW : Basisabfluss bei Trockenwetter. Quelle: Fohrer (2016).

## Slide 138: Hydrograph
Source: https://www.bbc.co.uk/scotland/education

## Slide 139: Discharge regime after Pardé
= Mean seasonal discharge behaviour of a river.
Pardé coefficient: ratio of mean monthly to mean annual discharge of each month: MQmi/MQa with i = month
Pluvial: influenced by rain. Maximum occurs delayed to the maximum of the raining season, depending on the residence time of the water in the EZG.
Nival: influenced by snowmelt.
Glacial: influenced by glacier melt.
Complex regime: Has several maxima in the year, e.g. pluvio-nival regime.

## Slide 140: Discharge regime: examples
Blau: Ems, Pegel Greven; rot: Inn, Pegel Passau; grün: Rhein, Pegel Mainz, Quelle: Fohrer (2016).

## Slide 141: Discharge regime along the River Danube
<100
100
200
300
400
500
1000
1500
2000
2500
>3000
m.a.s.l.

## Slide 142
4 Discharge
4.2 Monitoring

## Slide 143: Monitoring of discharge
The discharge (or flow) Q is defined as the quantity of water flowing through the
cross-section A of a watercourse within a unit of time.
Direct measurement
The volume of water flowing through a watercourse per unit of time is measured directly, e.g. with a bucket.
Cumbersome and only possible for small bodies of water
Indirect measurement
With the measurement of water level h, the discharge is determined via a discharge curve, where h = f (Q)
Measurement of velocity v and determination of cross-section A

## Slide 144: Venturi channel
Quelle: Wikimedia Commons contributors, CC BY-SA.
Narrowing of the flow cross-section A
Flow change: flowing to shooting
Water level clear measure of flow

## Slide 145: Monitoring weir
Thomson-/Dreieckswehr, Quelle: Fohrer (2016).
Weir = threshold, which is dimensioned in such a way that a shooting flow condition occurs
The discharge can be clearly determined from the water level upstream of the weir if the weir parameters are known.
Strong intervention in the flowing water is necessary!

## Slide 146: Tracer / dillution method
Tracer = marking substance (e.g. colour tracer or salt), which is discharged into the water at a known concentration.
Downstream, concentration is measured in the watercourse
The greater the dilution, the greater the discharge
https://www.openchannelflow.com/blog/an-overview-of-tracer-dilution-for-flow-rate-determination-in-natural-strea

## Slide 147: Water level gauges
Water level gauges are measuring devices of various designs for determining the water level in bodies of water.
http://www.computerart-3d.de/projekte/pegelhaus-querschnitt/

## Slide 148: Rating curve
In hydrology, a rating curve is a graph of discharge versus stage
… for a given point on a stream, usually at gauging stations, where the stream discharge is measured across the stream channel with a flow meter.

## Slide 149: Measuring and calibration via flow velocity
Mechanical measuring blade
Induction probe:
Magnetic field -> Water flow with free charge carriers induces electric voltage
ADCP (Acoustic Doppler Current Profiler):
Ultrasound Doppler effect (frequency shift) on scattering bodies in water
Sources: Mueller et al. (2013) and Ott HydroMet GmbH.

## Slide 150: Flow velocity field
Measurement of flow velocities across the watercourse cross-section
A (vertically and horizontally) non-uniform velocity v distribution occurs in a flow cross-section A. Causes: Roughness of the wetted cross-section, friction forces, turbulence.
Source: Fohrer (2016).

## Slide 151
4 Discharge
4.3 Regional and global discharge

## Slide 152: Water balance
Evaporation
Precipitation
Discharge
=
+
+
+/- storage

## Slide 153: Water cycle, global
The global water cycle. Illustration: GIZ (2020) with data from Trenberth et al. (2011).
Water reservoirs
Oceans, inland waters, glaciers, groundwater, atmosphere, soil water, organisms ...
Processes
Precipitation,
evaporation,
seepage,
Runoff

## Slide 154: Seasonal distribution of discharge
4.4 Niederschläge in Deutschland und Weltweit Niederschläge in Deutschland
Evapotranspiration
Precipitaion
Discharge
Elbe

## Slide 155: Global discharge
Li et al. 2018, Water

## Slide 156: The largest rivers (length)

## Slide 157: The largest rivers (discharge)

## Slide 158: Please answer the questions!
What is potential and what actual evapotranspiration?
What is interception?
What are reanalysis data?
How can precipitation, evapotranspiration and runoff be measured?
What are discharge regimes?
How much water flows in a second if river if the wetted river cross-section is 5 m2 and the flow velocity 2 ms-1?
What is the „Water Nexus“?

## Slide 159: Outline
Monday Nov. 18
The water cycle: From hydrological processes to observations,
presentation of topics, groupwork
Tuesday Nov. 19
The nexus water – energy – food. Water as a basic need, water as a threat: health, hydrological extremes, erosion,
Selection of topics, groupwork
Wednesday Nov. 20
Eco-hydrological modelling,
Groupwork
Thursday Nov. 21
Groupwork
Friday Nov. 22
Presentation of selected tasks, visiting PIK

## Slide 160: Possible task for the groupwork
Adaptation in a water related sector / field:
Cities (adaptation to flash floods, droughts, heat waves),
Nature based solutions in river basins or landscapes,
Re-thinking water storage (at different scales),
Adaptation to counteract erosion,
Integrating adaptation and mitigation,
Water re-use
…

## Slide 161
Thanks!